| Video Format |  | HDV (.m2t), DV (.dv) |
| --- | --- | --- |
|  | Audio Format |  | 16-bit/ 48kHz (Supports broadcast wav : .bwf) |
|  | Audio Control |  | Limiter, Gain, Phantom Power Supply (+48V) Input Level Select (-44/-20/-10dBu), Sens (0 to +24dB) |
|  | Recording Media |  | Removable type 2.5inch 120GB HDD *Max 10 hours recording |
|  | Input Jacks |  | Digital Video Input (IEEE 1394, 6pin, type), Analog Audio Input x 2 (XLR 3pin type) *Input Impedance : 4k ohms, Phones Output (Stereo mini type) *Output Impedance : 16 ohms *output Level :45mW, USB host (USB A), USB function (USB mini B), Network (Ethernet 100Base-Tx, RJ45 type), DC Input (XLR 4pin type) |
|  | Battery |  | AA type x 8 (NiMH or Alkaline) *Max 2 hours operation |
|  | External Battery |  | Li-Ion Battery (IDX Endura series etc.) *Max 10hours operation at 14.2V/7700Ah |
|  | Accessories |  | Removable HDD (F1-HD120) x 1, Battery Pack x 2 (1 as spare), USB cable (Y type with power supply), AC adaptor (9V / 2A, Roland PSB-1U) with XLR 4pin conversion cable, Owner's Manual |
|  | Optional Items |  | Carrying Bag (CB-F1), 120GB Removable HDD ( F1-HD120), V mount kit for mounting on video camera (F1-VMK1) |
| Size and Weight |
|  | Width |  | 111 mm | 4-3/8 inches |
|  | Depth |  | 179 mm | 7-1/16 inches |
|  | Height |  | 61 mm | 2-7/16 inches |
|  | Weight |  | 0.9 kg | 1 lbs. 15 oz. |
| Including HDD, excluding batteries |
| *The specifications are subject to change without notice. |