V-8

| Video Format | Video: NTSC or PAL (ITU601) PC-RGB: 640 x 480/120 Hz, 800 x 600/120 Hz, 832 x 624/75 Hz, 1024 x 768/80 Hz, 1152 x 864/80 Hz, 1152 x 870/75 Hz, 1280 x 1024/75 Hz, 1600 x 1200/60 Hz (RGB VH: positive/negative logic) * VESA DMT Version 1.0 Revision 10 conform. * The refresh rate is the maximum value of each resolution. |
| --- | --- |
| Video Sampling Rate | Video: 4:2:2 (Y:B-Y:R-Y), 8-bit, 13.5 MHz |
| Frame Synchronizer | 2 systems |
| Input Level and Impedance | Video (composite): 1.0 Vp-p, 75 ohms S-video: <Luminance signal> 1.0 Vp-p, 75 ohms <Chrominance signal> 0.286 mVp-p, 75 ohms (NTSC) / 0.3 mVp-p, 75 ohms (PAL) PC-RGB: 0.7 Vp-p, 75 ohms (H, V: 5 V TTL) |
| Output Level and Impedance | Video (composite): 1.0 Vp-p, 75 ohms S-video: <Luminance signal> 0 Vp-p, 75 ohms <Chrominance signal> 0.286 mVp-p, 75 ohms (NTSC) / 0.3 mVp-p, 75 ohms (PAL) |
| Connectors | Input Video (composite): BNC type x 7 (Ch 1 - 7) S-video: 4-pin mini DIN type x 4 (Ch 5 - 8) PC-RGB: D-SUB 15pin Shrink Type x 2 (Ch8: PC1 / PC2) * Inputs 5 - 8; however if S-video is simultaneously input to 5-8, S-video takes priority Output Video (composite): BNC type x 2, S-video: 4-pin mini DIN type x 1 Preview Output Video (composite): BNC type x 1 (OSD Menu) Monitor Output Video (composite): BNC type x 8 (Ch 1 - 8) |
| Remote Control Interfaces | MIDI IN: 5-pin DIN type x 1, MIDI OUT/THRU: 5-pin DIN type x 1 |
| Transition effects (more than 200 types) | Mix (Dissolve, Non-Additive Mix : NAM, Full-Additive Mix : FAM), Wipe (Hard edge wipe, Soft edge wipe), Key, Slide, Stretch, User Transition |
| Video effects | Still, Strobe, Afterimage, Feedback, Shake, Negative, Colorize, Find Edge, Silhouette, Mono Color, Emboss, Posterize, Color Pass, Luminance key, Chroma key, Flip, Multi, Mirror, Picture-in-picture |
| Power Supply | DC 9 V (AC Adaptor: Roland PSB-1U) |
| Current Draw | 2 A (Preliminary, AC Adaptor PSB-1U 0.4A) |
| Dimensions | 238 (W) x 315 (D) x 134 (H) mm (9-3/8 (W) x 12-7/16 (D) x 5-5/16 (H) inches) |
| Weight | 3.2 kg (7 lbs 1 oz) |
| Accessories | AC Adaptor, Power Cord, BNC to RCA video adapter x 4, mount screw for Video fader x 4, Owner's Manual |
| Options | Cross Fader: V-4CF |